Quantizer optimization
for LPC based voice coder: Codec 2
Wojciech Kaczmarski, M17 Project
m17project.org

---
Codec 2 - introduction
A free to use and open-source, low bitrate voice codec
Developed by David Rowe VK5DGR et al.
We are going to focus on the full rate, 3200 bps mode

---
Modeling speech
Speech is a sound pressure wave generated by vocal chords and filtered by an anatomical structure called the vocal tract
We can coarsely model the speech generation process using an excitation source and a filter
Both the excitation source and filter change their paremeters over time

---
Speech signal

---
Excitation and filtering
model

---
Excitation and filtering
The filter can be modeled with an all-pole digital filter
of order p:
H(z) = \frac{1}{A(z)} = \frac{1}{1+\sum_{k=1}^{p}a_k z^{-k}

---
20 ms speech frame

---
Excitation and filtering
Codec 2 obtains the filter coefficients a for each frame by computing p+1=11 autocorrelation values and solving a set of linear equations

---
DFT vs. |H(z)|

---
Polynomial to LSF
LSF – Line Spectral Frequency(ies)
A slight error in any value a of the A(z) polynomial representation of the all-pole filter might be catastrophic
Rationale for the conversion: LSF representation is much less susceptible to errors

---
Polynomial to LSF

---
Polynomial to LSF

---
LSF encoding
Codec 2 uses quantized delta encoding for the LSF parameters
LSF1 is mapped ‘as-is’
Every next LSF is encoded as a frequency shift from the previous one

---
LSF encoding
Eg. LSF1=145 Hz, the best entry is then 150
dlsp1
25
50
75
100
125
150
175
200

---
LSF encoding
LSF2=560 Hz, 560-150=410
dlsp1
25
50
75
100
125
150
175
200
dlsp2
300
325
350
375
400
425
450
475

---
LSF encoding
This process continues up to the last LSP
dlsp1
25
50
75
100
125
150
175
200
dlsp2
300
325
350
375
400
425
450
475
dlsp10
400
425
450
475
500
525
550
575
. . .

---
Quantizer improvements
Two approaches: improve the scalar quantizer – make quanta fit the actual data and its PDF
Use vector quantizer instead

---
Codebook generation
OpenSLR - free speech corpora for codebook generation
TED-LIUM(v2) has been successfully used for OpenACELP

---
Codebook generation
Centroid search – Linde-Buzo-Gray (LBG) or
k-means algorithm

---
LSF2-LSF1 difference
distribution
PDF
Codec 2 reference codebook
PDF optimized codebook
Frequency (Hz)

---
Vector quantizer
Proposal: use Multistage Vector Quantizer with Vector Split
Use a coarse codebook for all 10 LSFs
Split LSFs into subvectors of length {3,3,4} and use MSVQ to obtain better approximations of the input vector

---
Vector quantizer
Bit allocation for the quantizer:
6 bits for the coarse codebook
4 bits per stage for MSVQ
Use 3 stages for LSF1..3, 4 for LSF4..6 and 3 for LSF7..10
Total of 46 bits per frame (Codec 2 uses 50)

---
64
16
16
16
16
Codebook length

---
Vector quantizer
The resulting reconstructed vector is given by
v = Q_0(i_{0}) + \sum_{k=1}^{n_1}{Q_{1k}(i_{1k})} + \sum_{k=1}^{n_2}{Q_{2k}(i_{2k})} + \sum_{k=1}^{n_3}{Q_{3k}(i_{3k})}

---
MSVQ convergence
2D cross sections of the training sets used for Q_2x codebook generation
Axes: LSFs in cosine domain

---
MSVQ error distribution
Error distribution for the Q_2 codebook
Horizontal axis: absolute error bins, Euclidean distance
PDF
PDF \left( \left\lVert v-v_{inp} \right\rVert_2 \right)

---
Improving SQ - results
Computational complexity is the same
SD is reduced, but the change is likely to be imperceptible
Bitrate doesn’t change

---
Switch to VQ - results
Saves 200 bps
Cost – more multiplications to perform for the codebook search
SD rises, but the change should be negligible (assuming a simple handheld transceiver is used – low quality reproduction)

---
Thank you